## Slide 1: POINT CLOUD REGISTRATION
A PROJECT BY:
Soundharya
Nikita Wali
Srihari Gururaj

## Slide 2: OVERVIEW
Introduction
Point Cloud Registration
Iterative closest point (ICP)
Steps of ICP
Code Snippets
Output
Conclusion

## Slide 3: INTRODUCTION
In computer vision, pattern recognition, point set registration, also known as point cloud registration or scan matching, is the process of finding a spatial transformation (e.g., scaling, rotation and translation) that aligns two point clouds.
The process of finding such a transformation includes merging multiple data sets into a globally consistent model, and mapping a new measurement to a known data set to identify features.

## Slide 4: INTRODUCTION
Raw 3D point cloud data are typically obtained from Lidars and RGB-D cameras. 3D point clouds can also be generated from computer vision algorithms such as triangulation, bundle adjustment.
For 2D point cloud registration used in image processing and feature-based image registration, the point set may be 2D pixel coordinates obtained by feature extraction from an image, for example corner detection.
Point cloud registration has extensive applications in autonomous driving, motion estimation and 3D reconstruction, object detection and pose estimation mainly.

## Slide 5: ILLUSTRATIVE EXAMPLE OF POINT CLOUD REGISTRATION
Given a source point cloud and target point cloud
Determine correspondence pairs,(points, features)
Estimate a transformation that aligns the correspondences,
Apply the transformation to align the source and target

## Slide 6: ITERATIVE CLOSEST POINT
This is an algorithm that is employed to minimize the difference between two clouds of points.
This algorithm is often used to reconstruct a 2D or 3D surfaces from different scans, to achieve optimal path planning.

## Slide 7: ITERATIVE CLOSEST POINT
In the iterative closest point, one-point cloud is kept fixed. This fixed-point cloud is called the reference or target point cloud.
The other point also called the source point cloud is transformed to best match the reference.
This algorithm iteratively revises the transformation needed to minimize an error metric.
This error metric is usually a distance from the source to the reference point cloud such as the sum of squared distances between the coordinates of the matched pairs.

## Slide 8: ITERATIVE CLOSEST POINT
INPUT: Reference and source point clouds, initial estimation of the transformation to align the source to the reference, criteria for stopping the iterations.
OUTPUT: Refined transformation.
Steps of the algorithm:
For each point in the source point cloud, match the closest point in the reference point cloud
Estimate the combination of rotation and translation using a root mean square point to point distance metric minimization technique which will best align each source point to its match found in the previous step.
Transform the source points using the obtained transformation.
Iterate

## Slide 9: CONCLUSION

## Slide 10: QUESTIONS???